## Slide 1: APPLIED PHSICS
(SEAP-113)

## Slide 2: Quiz Rules
Only write short answer (in few words). Don’t go in details.
Any communication with others during the quiz will result in a zero score.
Time Limit is 10 mins.

## Slide 3: Sample Quiz Question
Question: In an AC circuit, the direction of current?
Question: Which type of current periodically changes direction?
Question: Which of the following is a measure of opposition to the flow of electric current?
Question: Voltage is also known as:
Question: Electric field is defined as the:
Question: What is the fundamental unit of electric charge?

## Slide 4: Quiz No. 1
Question 1: What happens to the electric field between two opposite charges as the distance between them increases?
Question 2: What is the relationship between voltage, current, and resistance in a circuit, according to Ohm's Law?
Question 3: In a series circuit, how does the total resistance compare to the individual resistances?
Question 4: Direction of Conventional current flows?
Question 5: The SI unit for electric current is?

## Slide 5: Quiz (Contd.)
Question 6: In an AC circuit, what does the frequency of the alternating current represent?
Question 7: If there is no net transport of charge in conductor, the electric current will be?
Question 8: If you double the voltage in a circuit, what happens to the current (assuming resistance remains constant)?
Question 9: What happens to the resistance of a conductor when its temperature increases?
Question 10: Resistance of a piece of material depends on?

## Slide 6: Introduction of Materials

## Slide 7: Introduction of Materials
Every material in nature has certain properties. These properties define the behavior of the materials. Material Science is a branch of electronics that deals with the study of flow of electrons in various materials or spaces, when they are subjected to various conditions.
Due to the intermixing of atoms in solids, instead of single energy levels, there will be bands of energy levels formed. These set of energy levels, which are closely packed are called as Energy bands.

## Slide 8: Types of Materials
The energy band in which valence electrons are present is called Valence band, while the band in which conduction electrons are present is called Conduction band. The energy gap between these two bands is called as Forbidden energy gap.
Electronically, the materials are broadly classified as Insulators, Semiconductors, and Conductors.

## Slide 9: Types of Material contd.
Insulators − Insulators are such materials in which the conduction cannot take place, due to the large forbidden gap. Examples: Wood, Rubber.
Semiconductors − Semiconductors are such materials in which the forbidden energy gap is small and the conduction takes place if some external energy is applied. Examples: Silicon, Germanium.
Conductors − Conductors are such materials in which the forbidden energy gap disappears as the valence band and conduction band become very close that they overlap. Examples: Copper, Aluminum.

## Slide 10: Valence & Conduction Band

## Slide 11: What is Semiconductor?

## Slide 12: Why Semiconductor?
Of all the three, insulators are used where resistivity to electricity is desired and conductors are used where the conduction has to be high.
The semiconductors are the ones which give rise to a specific interest of how they are used.
We need to have strong control over the conductivity of material.
By controlling conductivity we can actually turn on and turn off the device which is very much required in digital circuits.
Semiconductors are employed in the manufacture of various kinds of electronic devices, including diodes, transistors, and integrated circuits.
Such devices have found wide application because of their compactness, reliability, power efficiency, and low cost.
Due to their role in the fabrication of electronic devices, semiconductors are an important part of our lives. Imagine life without electronic devices. There would be no smartphones, radios, TVs, computers, video games, or advanced medical diagnostic equipment.

## Slide 13: Semiconductors
  What is conductor ?
  Copper (29 e-) is a good conductor as it has only one electron is its valence band
  Similarly the materials which has 4 electrons in their valence band are semiconductor materials
  Examples are Si (14 e-), Germanium (32 e-), Carbon (4 e-) etc.

## Slide 14: Semiconductors (contd.)
  Why silicon is widely used as compared to germanium?
  Reason is the atomic structure of both materials
  Silicon has 4 electrons in its 3rd shell while Germanium also has 4 electrons but in 4th shell
  Germanium valence e- require small energy to escape from the atom
  This makes Germanium unstable at high temperatures
  That’s why Silicon is most widely used in electronics

## Slide 15: Atomic Structure of Silicon & Germanium

## Slide 16: Doping of Semiconductors
The process of adding an impurity atoms into the semiconductor to increase its ability to conduct electricity is known as doping and the impure semiconductor is known as a doped semiconductor.
Doping is done to modify the electrical conductivity, carrier concentration, and other electrical characteristics of the semiconductor.
Types of Doping: There are two main types of doping:
  N-type doping: Introduces donor impurities that provide extra electrons (e.g., phosphorus, arsenic).
  P-type doping: Introduces acceptor impurities that create holes (missing electrons) (e.g., boron, gallium).
Dopant Atoms and Crystal Lattice: Dopant atoms replace some of the atoms in the crystal lattice of the semiconductor.
Creation of Charge Carriers:
  N-type doping creates excess negative charge carriers (electrons).
  P-type doping creates excess positive charge carriers (holes).

## Slide 17: Types of Semiconductors
Intrinsic Semiconductor
An intrinsic (pure) semiconductor, also called an undoped semiconductor or i-type semiconductor, is a pure semiconductor without any significant dopant species present. The number of charge carriers is therefore determined by the properties of the material itself instead of the amount of impurities.
Extrinsic Semiconductor
An extrinsic semiconductor is a semiconductor doped by a specific impurity which is able to deeply modify its electrical properties, making it suitable for electronic applications (diodes, transistors, etc.) or optoelectronic applications (light emitters and detectors).
Two Types of Extrinsic Semiconductor
P-type Semiconductor
N-type Semiconductor

## Slide 18: Types of Semiconductor

## Slide 19: Intrinsic Semiconductor Atomic Structure

## Slide 20: Extrinsic Semiconductor Atomic Structure

## Slide 21: Difference between Intrinsic & Extrinsic Semiconductors

## Slide 22: Why do we not use intrinsic semiconductor?
There are mainly three reasons:
Conductivity is low due to small number of charge carriers.
Number of free electron depends upon temperature, we can't control it.
Number of electrons are always equal to number of holes. Therefore, the current have a fixed ratio which we can not change.

## Slide 23: Semiconductors (contd.)
  Concept of Hole
  At room temp, some valence electrons
  absorbs energy and jump to the
  conduction band
  This causes a vacancy in the valence
  band of crystal called hole
  Recombination is the process when an e- falls in the hole

## Slide 24: Semiconductors (contd.)
  Concept of Free Electrons
  Free electron, unlike bound electrons within atoms, there is no specific atom or nucleus to which the electron is attached; it is not bound to any particular atomic nucleus and is free to move within the material.
  These electrons move freely and conduct electricity.

## Slide 25: Semiconductors (contd.)
  When voltage is applied to pure semiconductor, then e- can easily move towards positive side
  Known as electron current

## Slide 26: Semiconductors (contd.)
  Other type is hole current, which is explained well in diagram

## Slide 27: N-type Semiconductor
  n-type semiconductor: in which pentavalent materials added by doping to achieve certain electrical characteristics.
  Doped materials can be: Arsenic, Phosphorous, Bismuth and Antimony and called donner atoms
  Majority Charge Carriers are Free Electrons.
  Minority Charge Carries are Holes

## Slide 28: P-type Semiconductor
p-type semiconductor: in which trivalent materials added by doping to achieve certain electrical characteristics
Doped materials can be: Boron, Indium and Gallium and called acceptor atoms
Majority Charge Carriers are Holes.
Minority Charge Carries are Free Electrons

## Slide 29: Why N-Type and P-Type are electrically neutral?
N-type and P-type semiconductors are electrically neutral because the dopant atoms are itself neutral and they are introduced in the neutral semiconductor material. So, after the doping process, the whole material is electrically neutral.
In N-type, extra electrons from donor impurities create negative charges, but the semiconductor crystal's positively charged nuclei balance these out, maintaining neutrality.
Similarly, in P-type, acceptor impurities create positive "holes," but the negative charge of the remaining electrons in the crystal neutralizes this positive charge, resulting in an overall electrically neutral material.

## Slide 30: Semiconductors (contd.)

## Slide 31: Diode

## Slide 32: Diode Theory
  Intrinsic semiconductor doped with trivalent and pentavalent material, a boundary called pn-junction is formed between the p-type and n-type material
  This pn-junction is called diode.

## Slide 33: Diode Theory (contd.)
  For every electron which diffuse at the boundary, a positive charge is left in the n-region and a negative charge is left in the p-region
  This is barrier potential of diode which forbids further diffusion
  The region where this electron hole recombination occurs is called depletion region
  Certain amount of voltage equal to barrier potential is required to flow the electrons across the junction
  Typical barrier potential for Silicon diode is 0.7V and for Germanium 0.3V at 25°C

## Slide 34: Diode Theory (contd.)
  Typical diode structure and symbol is shown in fig
  p-type region is called Anode and n-type region is called Cathode
  pn-junction is in between the Anode and Cathode

## Slide 35: Biasing of Diode

## Slide 36: Biasing of Diode
In electronics, 'biasing' usually refers to a fixed DC voltage or current applied to a terminal of an electronic component such as a diode, in order to establish proper operating conditions for the component.
It is a crucial aspect of designing electronic circuits, especially in semiconductors like diodes, transistors.
Proper biasing ensures that the device operates in a stable and predictable manner.
Biasing a diode in electronics refers to the process of applying a specific voltage (or current) to the diode in order to control its electrical behavior and allow it to function in a desired way.
Two main types of diode biasing:
Forward Bias
Reverse Bias.

## Slide 37: Forward Biasing
  Biasing of diode is when it is connected with a voltage source
  When n-type material is connected with -ive and p-type material is connected with +ive side of source, it is called forward biasing
  Vbias should be greater than the barrier potential

## Slide 38: Forward Biasing (contd.)
  when voltage is greater then the barrier potential, free electrons crosses the barrier potential and move into the p-type material
  Electron current induced inside the diode

## Slide 39: Forward Biasing (contd.)
  More electron flow towards the depletion region, positive charge reduce and same is true for holes
  This causes the depletion region to becomes narrow
  Also the concept of energy hill

## Slide 40: Reverse Biasing
  Reverse biasing is the condition prevents the flow of current through diode.
  When p-type is connected with -ive and n-type is connected with +ive end of source.

## Slide 41: IV Characteristic Curve