## Slide 1: APPLIED PHYSICS
(SEAP-113)

## Slide 2: Full Wave Rectifier
  Full wave rectifier allows unidirectional current for entire 360° of input cycle
  It is combination of two half wave rectifiers
  For this purpose two diodes are used with a centre taped transformer which provides two separate voltages (out of phase) across its secondary winding
  One diode conducts and other diode is reverse biased during positive input cycle and vice versa
  As a result current is continuously flow through the load resistor

## Slide 3: Full Wave Rectifier (contd.)

## Slide 4: Full Wave Rectifier (contd.)

## Slide 5: Full Wave Rectifier (contd.)
  The average value of full wave rectifier can be calculated as:
  Equation shows that Vavg is approx. 63.6% of Vp (Ideal Diode Case)
  The frequency of full wave rectifier will be equal to

## Slide 6: Full Wave Rectifier (contd.)
  Another type of full wave rectifier is Bridge Rectifier

## Slide 7: Full Wave Rectifier (contd.)

## Slide 8: Full Wave Rectifier (contd.)
  the bridge output voltage in case of ideal approx. can be calculated as:
  By using the second approx. the bridge output voltage can be calculated as:

## Slide 9: Full Wave Rectifier (contd.)

## Slide 10: Power Supply Filtering
  For a power supply there must be a constant voltage amplitude without fluctuations
  The output of a Full wave or Half Wave rectifier is not constant
  There must be some filtering to smoothen the output of rectifiers

## Slide 11: Power Supply Filtering (Contd.)

## Slide 12: Power Supply Filtering (contd.)
  Capacitor input filter is used for filtering
  Capacitor is attached at the output of rectifier
  when the positive cycle arrived, diode becomes forward bias
  The capacitor start charging and it continues as voltage is increasing, when voltage starts decreasing, capacitor starts discharging and diode becomes reverse bias
  The time constant RC determines the discharging rate of capacitor
  Larger the time constant, lesser the capacitor discharge

## Slide 13: Power Supply Filtering (contd.)

## Slide 14: Power Supply Filtering (contd.)
  Capacitor quickly charge and slowly discharge during the complete cycle
  Variation in the capacitor voltage due to charging and discharging is known as ripple voltage
  Smaller the ripple, better the filtering

## Slide 15: Power Supply Filtering (contd.)
  Full wave rectifier has double the frequency as compare to half wave rectifier
  It is easier to filter the full wave rectifier output as there is short time between peaks
  When filtered with same load resistor and capacitor, full wave rectifier has small ripple as compared to half wave rectifier
  Because capacitor discharges less during the short intervals between full peaks

## Slide 16: Power Supply Filtering (contd.)

## Slide 17: Power Supply Filtering (contd.)
  The ripple factor (r) (amount of AC content present in DC output) is effectiveness of filter and defined as